## Slide 1
Week 24: the timing story survives its stress tests
CERA · Week 24
Robustness closed
±6 h
of arrival error never changes whether the city crashes — 12 of 12 shift arms agree on every crash decision.
GNN 2×2 delivered
~25%
of the dynamic-label difficulty gap closed by timing features; dynamic labels are +73% harder than static.
GISSR unblocked
10
audited findings sent to Gwen with reproduction to machine precision; fixes scoped to her repo.
feat/dynamic-flood-maps @ 1f21668 · Torch jobs 16802536 / 16803830 / 16805213 · memo v2 §4.6
SAY
We stress-tested every Week 23 timing claim — the story held, and the surrogate now tells the same story from the other side.
Notes: Frame: a course-heavy week spent hardening rather than expanding. Three results: (1) arrival-error robustness closes the last reviewer check on the dynamic-forcing memo; (2) the approved GNN 2x2 ran end to end — dynamic labels are genuinely harder, timing features close about a quarter of the gap; (3) the GISSR audit went to Gwen, unblocking the production flood-map batch. Everything is committed and pushed at 1f21668.

## Slide 2
Arrival error never changes IF — barely HOW MUCH
1 / 5
Chart: Δ end state vs unshifted (%)
| −6 h | −3 h | +3 h | +6 h
914_6 (1.30 m) | 1.9 | 1 | -2 | -2.2
880_9 (2.66 m) | 13.2 | 12.7 | -1.8 | -1.9
605_5 (3.76 m) | 0.05 | 0.15 | -0.36 | 0.21
0 / 12
shift arms that change any crash decision (N=100, paired seeds, t360)
914_6 ≤ 2.2%
605_5 ≤ 0.4%
880_9 +13% early only
largest end-state delta per storm across all four shifts
SAY
We slid every node's arrival by up to six hours in both directions. Whether the city crashes never changes; end states barely move — except in one place.
Notes: 12 runs: 4 uniform shifts x 3 storms, N=100, paired seeds against the unshifted arrival run. Crash fractions identical in every arm. End-state deltas: 914_6 up to 2.2% (monotone in shift, +/-6 brackets +/-3 as pre-registered); 605_5 at most 0.4% — the saturated storm absorbs arrival error entirely. 880_9 is the exception — next slide. This closes the arrival-uncertainty reviewer check in memo v2 section 4.6.

## Slide 3
The one sensitivity sits exactly on the tipping point
2 / 5
Storm 880_9 · 2.66 m surge · crash probability 0.98–1.00 — the crash-edge storm
Chart: mean failures before the surge peak (per run)
| −6 h (early) | −3 h | +3 h | +6 h (late)
pre-peak failures | 988 | 933 | 659 | 370
2.7×
more damage carried into the surge peak when water arrives early vs late
+13% / ≤2%
end-state shift for early vs late arrival — asymmetric, and confined to this storm
SAY
Early water means the system carries almost three times more damage into the peak — a fourth independent instrument finding the same regime boundary.
Notes: Mechanism, in Sandy terms: if the water reaches equipment hours before the worst of the surge, the grid is already degraded when the big hit lands — like ConEd fighting outages all afternoon before the 21:00 East 13th St failure. Pre-peak failures swing 370 to 988 across +6h to −6h. End state rises up to +13% (+315 nodes) with early arrival; later arrival moves it at most 2%. The sensitivity exists only in the tipping zone — the same 2.4–3.2 m band flagged by variance amplification (Wk22), end-state divergence (Wk23), and now the surrogate's difficulty ordering. For Dr. Lin: asymmetry is physical (damage accumulation is monotone in exposure time before the peak), not an artifact; N=100 per arm, paired seeds.

## Slide 4
World 2 agrees: timing opens outcome space
3 / 5
inputs: t0 mask
inputs: mask + timing
static
labels
dynamic
arrival
labels
0.1082
trained twin — reference
0.0981
−9.4% — timing helps even here
0.1877
+73% — arrival-ordered labels are harder
0.1653
closes ~25% of the dynamic gap
best val loss @ epoch 5 · identical seed / config / 5-way holdout · job 16805213
Even told when the water arrives, the surrogate can't recover static-world predictability — the residual gap is genuine unpredictability.
SAY
Dynamic labels are 73 percent harder to fit; arrival features claw back a quarter of that. The rest is the system being genuinely less predictable.
Notes: Val loss is the cross-cell metric (PR-AUC can't cross label rows: different prevalence). Twin fills the (static, mask) cell. Findings: (1) timing features help even on static labels (−9.4%) — they act as flood-severity covariates; (2) dynamic labels +73% — pre-registered and confirmed; (3) timing closes (0.1877−0.1653)/(0.1877−0.0981) ≈ 25%. Held-out difficulty ranks with saturation: 914_6 0.126 < 258_9 0.273 < gc2050 0.332 < 808_27 0.381 < 605_5 0.479 — same ordering as World 1 variance amplification. Honest caveat for Dr. Lin: single seed per arm; converged-regime val drift <0.003 over final two epochs, but a seed-repeat of one arm is the formal bound — offered as follow-up.

## Slide 5
A 4-minute smoke caught a silent metric bug
4 / 5
1
Smoke
3 arms, 1 epoch,
4 minutes
2
Fingerprint
CASCADE ≡ ALL
to 16 digits
3
Root cause
mask read at
x[:, −1]
4
Fix + re-smoke
−1 − N_TIMING_
FEATURES
5
Clean launch
3 × 90 min
production
0 GPU·h
of production compute lost — the bug would have silently equated the honest cascade-only metric with the inflated all-nodes one in every timing arm.
SAY
The identical-distribution fingerprint we adopted after earlier incidents caught this in the smoke, not in the paper.
Notes: The cascade-only metric recovered the initial-failure mask positionally as the last input column; appending timing features silently pointed it at time_to_peak/96 instead — nothing dropped, so CASCADE equaled ALL bit-for-bit in 4 of 5 held-out scenarios (605_5 escaped because its scaled timing values cross 0.5). One-line fix: index the mask at −1 − N_TIMING_FEATURES; the default build is unchanged by construction, so the trained twin's numbers stand. Re-smoke passed all sharp criteria before production launched. Process point: this is why every campaign starts with a smoke and a fingerprint gate.

## Slide 6
Decisions needed
5 / 5
Dr. Miura
Surge-clock anchor: peak vs onset
peak = Sandy-consistent, +21–58% persistent · onset = mean-neutral, fat two-sided tail. Gates the full timing retrain.
Gwen
GISSR production batch
direction pending replies to the audit · SLR by storm year (0.41 / 0.72 / 0.91 m) · spatial diversity: GeoClaw or gauge-scaled maps.
Dr. Lin
Rigor follow-ups
single-seed caveat: seed-repeat of one 2×2 arm offered · N_MC 200–300 learning-curve question · ordering of reviewer checks.
SAY
The one decision that gates this week is the surge-clock anchor — everything else can proceed in parallel.
Notes: Ask order: (1) surge-clock anchor — recommend peak (Sandy call-volume record argues for it; +21–58% persistent end-state effect), but present onset honestly (mean-neutral with a fat two-sided tail). This decision picks the canonical dynamic labels for the full timing retrain, which also waits on Gwen's corrected maps. (2) GISSR: batch design once Gwen replies; SLR added by storm year; spatial-diversity question is an advisor call. (3) Dr. Lin: offer the seed-repeat proactively; N_MC 200–300 as a learning-curve experiment. Next week preview: Sandy hindcast timeline check on the existing arrival-ordered GeoClaw runs — zero new simulation, converts the timing claim from model-conditional to empirically anchored.