## Slide 1
The failed-by curve only rises because the simulator has no recovery. Recovery would be a second rising curve, not a falling one
Chart: Schematic, not data: share of sites vs time after the peak
| 0 | 6 h | 24 h | 48 h | 96 h | 1 wk | 2 wk | 4 wk
Ever failed (what the surrogate predicts today) | 5 | 20 | 45 | 60 | 70 | 72 | 72 | 72
Restored (not modelled yet) | 0 | 0 | 2 | 6 | 14 | 40 | 60 | 70
Out of service now = the gap | 5 | 20 | 43 | 54 | 56 | 32 | 12 | 2
What the code says
The engine never brings a site back. A failed site keeps its one fail time (cascade_joint.py:232); the code comment reads "dead stays dead" (intra_telecom.py:67).
So every label row is 0…01…1. There is no recovery event in the training data (data.py:153), and a surrogate cannot learn what its labels do not contain.
A restoration layer exists but is outside the cascade loop. downtime.py gives days-to-restore per site for the economic handoff; its times are placeholders awaiting verification (restoration_curves.yaml).
Proposed: keep recovery out of the surrogate for now and enforce the rising order. Add recovery to the simulator first, with verified restoration times; then the surrogate gets a second head for "restored by t".
Reversible states: Putter, Fiocco & Geskus 2007, Stat. Med. 26:2389. Loss then restoration: Bruneau et al. 2003, Earthquake Spectra 19:733.
Say: You asked: add recovery, or enforce the rising order? The simulator never brings a site back, so the labels contain no recovery and the surrogate cannot learn it. Recovery would be a second rising curve, sites restored. What is out of service is the gap between the two, as after Sandy: up within hours, down over days.
Notes: You asked: add recovery, or enforce the rising order? The simulator never brings a site back, so the labels contain no recovery and the surrogate cannot learn it. Recovery would be a second rising curve, sites restored. What is out of service is the gap between the two, as after Sandy: up within hours, down over days.

## Slide 2
Where the rising order is enforced makes no measurable difference to fit: the falls were many but tiny
cell (labels, inputs) | independent head | + running max | + sort | + isotonic | hazard head | pairs that fall | median fall
static, mask | 0.10824 | 0.10825 | 0.10824 | 0.10823 | 0.10796 | 6.8 % | 0.00003
static, mask + timing | 0.09808 | 0.09808 | 0.09808 | 0.09807 | 0.09796 | 7.8 % | 0.00001
dynamic, mask | 0.18774 | 0.18773 | 0.18774 | 0.18774 | 0.18798 | 4.0 % | 0.00002
dynamic, mask + timing | 0.16529 | 0.16526 | 0.16528 | 0.16528 | 0.16508 | 6.3 % | 0.00013
What the audit measured (8 saved checkpoints, no training)
Output-side fixes move val loss by at most 0.00002. Sort and isotonic never worsen it, as proved; running max sometimes does.
The falls are common but tiny. 4–8 % of pairs fall; the median fall is 0.00001–0.0001 in probability. Per run, 36–51 of 6,231 sites fall by more than 0.01 and 2–6 by more than 0.05; the largest single fall is 0.16–0.33.
The hazard head differs by more than any fix does: ±0.0003 on validation; −0.0145 to +0.0092 on held-out storms, where a fix moves at most 0.0006. That is a different trained model, not the constraint.
What this changes
Last week I gave the count; this is the size. The falls are a consistency defect, not an accuracy one.
Fit cannot choose between the two sides. I keep the hazard head because its outputs are per-window hazards: what the survival likelihood trains on next, and what a recovery head would reuse. The rare large falls also disappear with no extra step.
Sort or isotonic regression is the free patch for checkpoints already trained.
Val loss: BCE averaged over six site types, 3,400 runs, seed 42; 18,693 (site, horizon-pair) entries per run. Torch job 18896971; each head's number reproduces its saved val loss. A fall is a drop above 1e-6.
Say: Last week I told you 4 to 8 percent of pairs fall. This week I measured how far: typically a hundred-thousandth to a ten-thousandth in probability. So enforcing the order, inside the model or after it, does not change the fit. I keep the hazard head for what it enables next, not for accuracy.
Notes: Last week I told you 4 to 8 percent of pairs fall. This week I measured how far: typically a hundred-thousandth to a ten-thousandth in probability. So enforcing the order, inside the model or after it, does not change the fit. I keep the hazard head for what it enables next, not for accuracy.

## Slide 3
Next: train the hazard head on the survival likelihood, the first step that can change timing accuracy
Why this step
Shape is fixed, accuracy is not. Arrival-timed labels still cost +73 % val loss with mask-only inputs (0.1082 → 0.1877), and timing inputs close about a quarter of that gap (0.1653).
The hazard head already outputs what a survival likelihood scores: the chance of failing in each window, given survival so far. One loss term per site at its actual failure window, instead of four separate yes/no questions.
One variable changes. Same four windows, same labels, same inputs, same seed. Val BCE stays reported so the numbers remain comparable.
Order of work
1. Seed check. The hazard head looked better on 4 of 5 held-out storms for dynamic + timing (up to −0.0145). The constraint itself is worth at most 0.0006 there, and other cells differ by up to +0.0092 the other way. Rerun both heads at seeds 43 and 44 with the torch seed set explicitly; --seed now fixes only the split and shuffle.
2. Survival loss. Flag off by default, fingerprint against hand-computed cases, written predictions, then the four-cell run on Torch.
3. Finer windows (3 h). Needs a new Torch label campaign on the 3-h grid; the existing labels are stamped on the 6-h grid.
Later: recovery as a second head, once the simulator produces restore times.
Still open from 24 Sept: surge-clock anchor (peak or onset) · run the 3-h Torch campaign or state Week 23 magnitudes as grid-conditional · report tipping share with its grid.
Hazard networks: Gensheimer & Narasimhan 2019, PeerJ 7:e6257; Kvamme & Borgan 2021, Lifetime Data Anal. 27:710. Inconsistent binary outputs: Cao et al. 2020.
Say: Next week, first a seed check, because the hazard head's held-out gain cannot come from the constraint itself. Then I change one thing, the training loss: the hazard head gives the chance of failing in each window given survival so far, which a survival likelihood scores directly. Predictions are written before each run.
Notes: Next week, first a seed check, because the hazard head's held-out gain cannot come from the constraint itself. Then I change one thing, the training loss: the hazard head gives the chance of failing in each window given survival so far, which a survival likelihood scores directly. Predictions are written before each run.

## Slide 4
Backup: when failure is permanent, sorting or isotonic regression cannot raise the loss. A running maximum can
reading of outputs (−2, 0, 1, −1) | 6 h | 24 h | 48 h | 96 h | note
as trained (independent head) | 0.119 | 0.500 | 0.731 | 0.269 | falls at 96 h
+ running max | 0.119 | 0.500 | 0.731 | 0.731 | only raises values
+ sort | 0.119 | 0.269 | 0.500 | 0.731 | same four values, reordered
+ isotonic | 0.119 | 0.500 | 0.500 | 0.500 | closest rising curve
hazard head (same four numbers) | 0.119 | 0.560 | 0.882 | 0.913 | chained hazards, cannot fall
Why sort cannot hurt
Labels never recover, so each row is 0…01…1. On a 0 the loss rises with the predicted probability; on a 1 it falls.
Sorting is a chain of swaps of out-of-order neighbours. If the two labels are equal, nothing changes. If they are (0, 1), the smaller value moves to the 0 and the larger to the 1: both terms improve.
Why isotonic cannot hurt, and running max can
Isotonic regression replaces each falling stretch by its mean. Inside such a stretch the early values average above the mean and the late values below it, so pulling them to the mean helps the 0s and the 1s (Jensen's inequality).
A running maximum only raises values, which costs on every 0 it touches: worse in 36 % of 1,000,000 random cases.
Holds for BCE and Brier (scripts/week28_mono_enforce_fingerprint_v1.py). Sorting: Chernozhukov et al. 2010, Econometrica 78:1093. Isotonic: Barlow et al. 1972.
Say: Only if asked. Same four numbers, five readings. Sorting and isotonic regression cannot make the loss worse when labels never recover; the argument is two lines each and I checked it on a million cases. A running maximum has no such guarantee.
Notes: Only if asked. Same four numbers, five readings. Sorting and isotonic regression cannot make the loss worse when labels never recover; the argument is two lines each and I checked it on a million cases. A running maximum has no such guarantee.