## Slide 1
The surrogate knows which sites fail and when, but not how many: it reads a small storm as a big one and a big one as smaller
Chart: Predicted ÷ simulated failures by 96 h, five unseen storms (1.0 = correct)
| 914_6 (2.2 m) | 258_9 (3.4 m) | GeoClaw 2050 | 808_27 (3.7 m) | 605_5 (4.5 m)
static labels, with timing inputs | 3 | 0.81 | 0.82 | 0.89 | 0.89
dynamic labels, with timing inputs | 3.8 | 0.7 | 0.62 | 0.7 | 0.72
The 8 saved models, re-scored with no retraining
Works: which sites, and when. Ranking quality (AP) 0.92–0.93. Among sites that fail, the predicted time window is the right one for 86 % (static labels) and 73–75 % (dynamic). One storm takes 11 ms; the simulator takes 0.2–1.5 s.
Does not work: how many. Per-run count error at 96 h is 41–54 %.
A lookup table does better. "Take the training storm with the closest number of flooded sites and reuse its failure frequencies": count error 19 %, and a lower log loss than the model on validation in all 8 models.
Where the model wins: the GeoClaw map (a different flood model) and the storm above the training range, where no similar storm exists to look up.
Written before the run: 5 predictions. Calibration and speed held. Three missed: beat the lookup on validation; beat it on 3 of 5 unseen storms; count error within 10–20 %.
Torch job 19301158: all gates pass, every model reproduces its saved loss. Non-seed sites only (the flood's direct hits are an input). Validation = 3,400 runs; each unseen storm = 1,000 runs.
Say: You asked for numbers. The model is good at which sites fail and in which time window, and it is fast. But it gets the size of the cascade wrong: three to four times too many failures for a small storm, a tenth to four tenths too few for big ones. A simple lookup table beats it on storms like those it trained on.
Notes: You asked for numbers. The model is good at which sites fail and in which time window, and it is fast. But it gets the size of the cascade wrong: three to four times too many failures for a small storm, a tenth to four tenths too few for big ones. A simple lookup table beats it on storms like those it trained on.

## Slide 2
Why: each site sees only two links away, so most sites get the same input in every storm
Chart: By storm size (peak water level at the Battery, m)
| 1.9 | 2.1 | 2.3 | 2.4 | 2.7 | 3.0 | 3.2 | 3.4 | 3.7 | 4.0 | 4.3 | 4.7
Sites with no flooded site within two links (%) | 88.3 | 84.1 | 80.4 | 76.5 | 73.2 | 69.1 | 66.8 | 65.4 | 64.2 | 61.4 | 59.3 | 58.5
Of those sites, the share that really fails by 96 h (%) | 0.3 | 1.2 | 5.4 | 14.9 | 16.1 | 18.2 | 18.1 | 18.4 | 18.6 | 15.7 | 13.7 | 14.5
What the model can and cannot know
Two rounds of message passing, nothing city-wide. A site's answer depends only on sites within two dependency links of it.
Most sites have no flooded site that close: 59–88 % of them, in every storm. Their input is then identical in every storm.
Shown on the model itself: 3,481 sites got exactly the same output in a small storm (914_6) and a large one (605_5). 24 of them fail in the small storm, 610 in the large one.
So those sites get one average answer: too high in a small storm, too low in a big one. The lookup wins because it is keyed on storm size. More storms alone cannot fix this.
Status: the mechanism is shown on the code (outputs identical to the last bit). Whether it explains the whole count error is what the next slide tests.
Production graph: 6,231 sites, 37,355 directed links. Simulator runs with static labels, 20 per storm, 67 GISSR storms. Reaching nearly every site would take 8–10 links.
Say: Why does it misjudge size? The model passes messages over two links. A cell tower in the Bronx with nothing flooded nearby is told nothing about whether Lower Manhattan is under water, so it gets the same answer in every storm: an average. That average is too high for a small storm and too low for a big one.
Notes: Why does it misjudge size? The model passes messages over two links. A cell tower in the Bronx with nothing flooded nearby is told nothing about whether Lower Manhattan is under water, so it gets the same answer in every storm: an average. That average is too high for a small storm and too low for a big one.

## Slide 3
Telling every site how big the storm is fixes the count: error falls from 41–54 % to 15–17 %, and the model now beats the lookup
What changes (one switch, off by default)
Every site also gets 7 numbers for the whole storm: how much of each of the six systems the water knocked out, and the total. With timing inputs, 3 more: storm-wide averages of arrival, duration and hours before the peak.
Inputs only. Nothing from the cascade outcome. +0.4 % parameters. With the switch off the inputs are bit-for-bit unchanged.
Written before training (17 old storms, two seeds)
C1 validation count error at 96 h at most 30 % (was 41–54 %).
C2 small unseen storm 914_6 within ±50 % (was 3–4 times too many).
C3 unseen storm 258_9 within ±12 % (was 18–33 % too few).
C4 log loss clearly lower in all four cells; half the gap to the lookup closed (static).
cell (labels, inputs) | count error, validation | 914_6: predicted ÷ simulated | 258_9: predicted ÷ simulated | log loss, validation | lookup
static, mask | 0.486 → 0.149 | 3.28 → 1.09 | 0.78 → 1.02 | 0.0814 → 0.0449 | 0.0709
static, +timing | 0.414 → 0.153 | 3.01 → 1.09 | 0.82 → 1.02 | 0.0727 → 0.0446 | 0.0709
dynamic, mask | 0.539 → 0.165 | 4.27 → 1.13 | 0.67 → 0.97 | 0.1617 → 0.0708 | 0.0953
dynamic, +timing | 0.459 → 0.161 | 3.88 → 1.05 | 0.71 → 0.91 | 0.1403 → 0.0688 | 0.0953
Verdicts: all six pass (S1, C1–C5). Against the lookup (log loss; validation + 5 unseen storms, 4 cells): the model won 7 of 24 before and wins 23 of 24 now. The one loss: 258_9, dynamic + timing (0.168 against 0.163).
Arrow: without → with the storm-size input, mean of seeds 1 and 2 (they agree within 0.02 on count error, one exception in backup). Old 17 storms. Torch jobs 19358319 (training) and 19358351 (scoring): 20 of 20 pass every gate.
Say: It worked, and it worked the way we wrote down beforehand. With one extra input, the count error drops from about half to about one sixth, the small storm is no longer read as a big one, and the model now beats the lookup table almost everywhere. Sandy version: once every operator knows how much of each system is under water, the damage estimate comes out the right size.
Notes: It worked, and it worked the way we wrote down beforehand. With one extra input, the count error drops from about half to about one sixth, the small storm is no longer read as a big one, and the model now beats the lookup table almost everywhere. Sandy version: once every operator knows how much of each system is under water, the damage estimate comes out the right size.

## Slide 4
48 new GISSR storms separate storm size from storm speed. They add water levels and timing, not new flood patterns
Chart: Hours the typical flooded site is wet before the peak, by storm size
| 1.911 | 1.922 | 1.922 | 2.017 | 2.102 | 2.15 | 2.166 | 2.272 | 2.292 | 2.369 | 2.563 | 2.632 | 2.797 | 3.092 | 3.24 | 3.372 | 3.444 | 3.64 | 3.745 | 4.458 | 1.935 | 2.002 | 2.07 | 2.138 | 2.205 | 2.272 | 2.339 | 2.408 | 2.477 | 2.544 | 2.614 | 2.684 | 2.755 | 2.807 | 2.88 | 2.959 | 3.011 | 3.089 | 3.142 | 3.232 | 3.299 | 3.342 | 3.407 | 3.498 | 3.557 | 3.632 | 3.687 | 3.759 | 3.827 | 3.89 | 3.963 | 4.027 | 4.105 | 4.153 | 4.23 | 4.297 | 4.363 | 4.437 | 4.508 | 4.572 | 2.103 | 2.439 | 2.777 | 3.116 | 3.458 | 3.8 | 4.13 | 4.722
20 delivered storms | 1.86 | 1.8 | 1.89 | 1.6 | 2.22 | 2.46 | 1.69 | 2.08 | 2.42 | 2.6 | 1.52 | 2.2 | 12.92 | 3.54 | 3.28 | 2.55 | 13.95 | 14.48 | 13.45 | 26.38
40 new training storms | 2 | 12.05 | 2 | 11.91 | 2 | 11.96 | 2 | 11.9 | 1.99 | 11.99 | 2 | 12.02 | 2 | 12 | 2.01 | 11.91 | 2.05 | 12.02 | 1.99 | 11.96 | 2 | 11.77 | 2.01 | 11.41 | 2.02 | 12.01 | 1.99 | 12.08 | 2.05 | 12.6 | 2.42 | 11.97 | 2.42 | 11.91 | 2.98 | 12.29 | 2.62 | 11.87 | 2.63 | 12.72
8 new held-out storms | 3.77 | 10.65 | 3.96 | 9.26 | 4.02 | 6.68 | 4.06 | 6.72
How they were chosen, and what they are
A written rule, fixed before any cascade result. From 73,940 catalogue storms: 40 levels evenly spaced from 1.9 to 4.6 m (old training stopped at 3.6 m), alternating fast storms (site wet 2 h before the peak) and slow ones (12 h).
Size and speed are now separate. In the 20 delivered storms the big ones were also the slow ones (correlation 0.82); in the new 40 it is 0.07.
Labels are done: 1,000 simulator runs per storm, both label types. The wrapper reproduces the old campaign record for record.
Limit: a GISSR map is almost fixed by the peak level (rank correlation 0.9998 with the number of wet sites). New flood patterns need a different flood model.
For Gwyn: her 20 maps are reproduced by one-hour time steps (13 wet/dry differences among 5,827 wet sites), not by each storm's own time steps (228). Which did she intend?
data/flood/gissr48_manifest_v1.csv. Label campaign: Torch job 19306610, 98 tasks, identity checks pass at 1,000 runs. 8 held out: 7 between training levels, 1 above the range (4.72 m).
Say: You asked for more flood maps. I generated 48 new storms from Gwyn's model by a rule written in advance, and ran the simulator on all of them. They fix a flaw in the first 20, where big storms were always slow ones. One caution: these maps differ in level and timing, not in where the water goes.
Notes: You asked for more flood maps. I generated 48 new storms from Gwyn's model by a rule written in advance, and ran the simulator on all of them. They fix a flaw in the first 20, where big storms were always slow ones. One caution: these maps differ in level and timing, not in where the water goes.

## Slide 5
Under arrival labels cascades are larger, and above 3.6 m a slow storm does more damage than a fast one of the same size
Chart: Mean failed sites by 96 h (1,000 runs per storm)
| 1.935 | 2.002 | 2.07 | 2.103 | 2.138 | 2.205 | 2.272 | 2.339 | 2.408 | 2.439 | 2.477 | 2.544 | 2.614 | 2.684 | 2.755 | 2.777 | 2.807 | 2.88 | 2.959 | 3.011 | 3.089 | 3.116 | 3.142 | 3.232 | 3.299 | 3.342 | 3.407 | 3.458 | 3.498 | 3.557 | 3.632 | 3.687 | 3.759 | 3.8 | 3.827 | 3.89 | 3.963 | 4.027 | 4.105 | 4.13 | 4.153 | 4.23 | 4.297 | 4.363 | 4.437 | 4.508 | 4.572 | 4.722 | 1.935 | 2.07 | 2.205 | 2.339 | 2.477 | 2.614 | 2.755 | 2.88 | 3.011 | 3.142 | 3.299 | 3.407 | 3.557 | 3.687 | 3.827 | 3.963 | 4.105 | 4.23 | 4.363 | 4.508 | 2.002 | 2.138 | 2.272 | 2.408 | 2.544 | 2.684 | 2.807 | 2.959 | 3.089 | 3.232 | 3.342 | 3.498 | 3.632 | 3.759 | 3.89 | 4.027 | 4.153 | 4.297 | 4.437 | 4.572 | 2.103 | 2.439 | 2.777 | 3.116 | 3.458 | 3.8 | 4.13 | 4.722
static labels (all 48) | 133 | 170 | 239 | 270 | 294 | 368 | 580 | 824 | 1066 | 1167 | 1265 | 1396 | 1522 | 1604 | 1674 | 1692 | 1726 | 1779 | 1845 | 1894 | 1971 | 1994 | 2017 | 2086 | 2132 | 2158 | 2198 | 2226 | 2251 | 2290 | 2330 | 2360 | 2392 | 2409 | 2419 | 2443 | 2464 | 2478 | 2500 | 2504 | 2508 | 2523 | 2540 | 2556 | 2572 | 2584 | 2598 | 2660
arrival labels, fast storms | 136 | 248 | 379 | 844 | 1309 | 1578 | 1810 | 1864 | 2004 | 2278 | 2768 | 3052 | 3342 | 3328 | 3215 | 3187 | 3120 | 3625 | 3090 | 3159
arrival labels, slow storms | 197 | 353 | 623 | 1145 | 1619 | 1815 | 1953 | 2190 | 2199 | 3017 | 3054 | 3293 | 3494 | 3422 | 3633 | 3630 | 3652 | 3648 | 3717 | 3701
arrival labels, held-out | 353 | 1225 | 1855 | 2259 | 3308 | 3444 | 3640 | 3749
What the simulator says
Static labels rise smoothly with the water level, from 130 to 2,660 failed sites; the steep part is between about 2.2 and 2.6 m.
Arrival labels give 2–50 % more failures on the same storm, with a second step near 3.2 m (2,300 to 3,000 sites).
Size is not everything: above 3.9 m slow storms end at 3,630–3,720 failed sites and fast ones at 3,090–3,190 (one exception, at 4.23 m). The fast ones also vary about three times as much from run to run.
Why it matters: two storms of the same size can end 500 sites apart, so storm size alone cannot be the whole input.
Source: 1,000 simulator runs per storm and label type (Torch job 19306610, 96 of 96 complete). The identity check reproduces the old campaign record for record.
Static: all flooded sites switch off at once. Arrival: each site switches off when the water reaches it. Same dice in both. Clock anchored at the peak, 6-hour grid.
Say: This is what the new storms teach us about the simulator itself. When each site switches off as the water reaches it, cascades are larger, and for the big storms a slow one ends about 500 sites above a fast one of the same size. So two storms of the same size can end differently.
Notes: This is what the new storms teach us about the simulator itself. When each site switches off as the water reaches it, cascades are larger, and for the big storms a slow one ends about 500 sites above a fast one of the same size. So two storms of the same size can end differently.

## Slide 6
Old + new storms: more storms help most above the old range, the storm-size input helps everywhere, and together they halve the error
Chart: Mean log loss on the 13 unseen storms (lower is better)
| static labels, mask input | dynamic labels, timing inputs
17 storms | 0.1079 | 0.2292
57 storms | 0.0883 | 0.1789
lookup table from 57 storms | 0.0743 | 0.1631
17 storms + storm size | 0.0633 | 0.1262
57 storms + storm size | 0.0552 | 0.0994
Same model, same number of training runs
More storms alone: log loss down 18 % (static) and 22 % (dynamic); 26–44 % on all 5 storms above the old range. The size error stays: the two small storms go from 3.3–3.9 to 4.2–5.2 times the simulated count, and the lookup still wins on 9–11 of 12 GISSR storms.
Storm size alone: down 41 % and 45 %. Better than more storms alone on 11 and 12 of the 13 storms.
Both: down 49 % and 57 %. Above the old range, 7–42 % below storm size alone on all 5 storms; counts there within 5 %.
Watch: with both, the two smallest storms are over-counted by 26–57 % (with 17 storms: 24 % under to 8 % over).
Interim: two of three arms, two of four cells, one seed each. No verdict on the written predictions (M1–M7, L1): they need the all-runs arm, which the cluster cancelled 2 h 15 min into a 4-hour run.
Mean log loss on non-seed sites over the 13 unseen storms (5 old, 8 new; 1,000 runs each). 57 storms = 17 old + 40 new, 13,600 training runs as for 17. Seed yardstick (old model against its retrain): at most 0.002 static, 0.012 dynamic. Torch jobs 19358745, 19358746.
Say: This is the comparison you asked for. Adding the new storms helps, mostly for storms bigger than anything in the old set. But it does not fix the size problem by itself; the storm-size input does. With both, the error is about half of where we started. It is an interim result: one seed, and the run that uses all the new simulator runs was cancelled by the cluster.
Notes: This is the comparison you asked for. Adding the new storms helps, mostly for storms bigger than anything in the old set. But it does not fix the size problem by itself; the storm-size input does. With both, the error is about half of where we started. It is an interim result: one seed, and the run that uses all the new simulator runs was cancelled by the cluster.

## Slide 7
Next: finish the more-storms runs, a storm summary that follows the clock, and flood maps with new patterns. Four decisions for you
Next steps
1. Finish the more-storms comparison. The all-runs arm (cancelled by the cluster), the second seed, and the other two cells, which also tell us whether the per-site timing inputs still help.
2. Storm summary by hour. Today's summary is one number per system for the whole storm. Under dynamic labels the 6-hour count on the two largest unseen storms is still 10–20 % low: give the share under water hour by hour.
3. Maps with new flood patterns. GISSR storms differ in level and timing only. The real test is a different flood model; the one GeoClaw map is still 13–17 % low under dynamic labels.
4. Then the survival loss from last week's plan, on the model that counts correctly.
Decisions I need (three open since 24 Sept, one new)
Surge clock: the phone-demand surge is anchored at the flood's peak. Keep the peak, or anchor at first arrival of water? All new labels use the peak.
Week 23 magnitudes: quote them as "on a 6-hour grid" (my proposal), or rerun on a 3-hour grid at about twice the compute?
Reporting rule: tipping share is always quoted with its grid; the surrogate's targets stay at 6, 24, 48 and 96 h.
New: the new depth tables come from Gwyn's unpublished model and sit in the public repo, as the first 20 do. Is that acceptable?
Correction on record: no earlier training run set the PyTorch seed, so each started from different random weights. This week's runs set it (seeds 1 and 2).
Tipping share by grid (880_9, 6 / 3 / 1 h): static 0.00 / 0.16 / 0.26, arrival 0.03 / 0.23 / 0.34.
Say: Next: finish the runs the cluster cancelled, make the storm summary follow the clock, and test on flood maps that look different, not just bigger. And I still need your call on three things from September, plus one new question about publishing depth tables that come from Gwyn's model.
Notes: Next: finish the runs the cluster cancelled, make the storm summary follow the clock, and test on flood maps that look different, not just bigger. And I still need your call on three things from September, plus one new question about publishing depth tables that come from Gwyn's model.

## Slide 8
Backup: the numbers sheet against its five written predictions
prediction (written 6 Oct, before the run) | result | verdict
P1 On validation the model beats all three baselines (8 models) | lookup has the lower log loss in all 8 | MISS
P2 On unseen storms the model beats the lookup on 3 of 5 (4 cells) | wins on 2, 2, 1, 2 of 5 | MISS
P3 Validation count error at 96 h ≤ 10 % (static), ≤ 20 % (dynamic) | 49 %, 41 %, 54 %, 46 % | MISS
P4 Validation calibration error ≤ 0.02 at every horizon | at most 0.0094 | PASS
P5 One forward pass ≤ 50 ms | 11 ms on an L40S | PASS
validation, hazard head | static, mask | static, +timing | dynamic, mask | dynamic, +timing
log loss, model | 0.0813 | 0.0725 | 0.1619 | 0.1406
log loss, lookup | 0.0709 | 0.0709 | 0.0953 | 0.0953
count error at 96 h, model | 0.486 | 0.414 | 0.539 | 0.461
count error at 96 h, lookup | 0.191 | 0.191 | 0.184 | 0.184
right time window, given failure | 0.859 | 0.863 | 0.725 | 0.749
Log loss and counts on non-seed sites. Lookup = failure frequencies of the training storm with the closest number of flooded sites. Torch job 19301158; scripts/week29_numbers_table_v1.py.
Say: Only if asked. Five predictions were written before the run; two held and three missed. The misses are what pointed to the two-link problem.
Notes: Only if asked. Five predictions were written before the run; two held and three missed. The misses are what pointed to the two-link problem.

## Slide 9
Backup: the storm-size test on each of the five unseen storms, and its limits
predicted ÷ simulated failures by 96 h: without → with | static, mask | static, +timing | dynamic, mask | dynamic, +timing
914_6 (2.2 m) | 3.28 → 1.09 | 3.01 → 1.09 | 4.27 → 1.13 | 3.88 → 1.05
258_9 (3.4 m) | 0.78 → 1.02 | 0.82 → 1.02 | 0.67 → 0.97 | 0.71 → 0.91
GeoClaw 2050 | 0.79 → 1.02 | 0.82 → 1.01 | 0.59 → 0.87 | 0.63 → 0.83
808_27 (3.7 m) | 0.78 → 1.01 | 0.89 → 1.02 | 0.59 → 0.99 | 0.71 → 0.96
605_5 (4.5 m) | 0.82 → 1.02 | 0.88 → 1.08 | 0.62 → 1.04 | 0.72 → 1.02
log loss with the storm-size input ¦ lookup | static, mask | static, +timing | dynamic, mask | dynamic, +timing
914_6 (2.2 m) | 0.012 ¦ 0.019 | 0.012 ¦ 0.019 | 0.016 ¦ 0.022 | 0.015 ¦ 0.022
258_9 (3.4 m) | 0.055 ¦ 0.073 | 0.055 ¦ 0.073 | 0.149 ¦ 0.163 | 0.168 ¦ 0.163
GeoClaw 2050 | 0.057 ¦ 0.166 | 0.057 ¦ 0.166 | 0.147 ¦ 0.502 | 0.192 ¦ 0.502
808_27 (3.7 m) | 0.062 ¦ 0.071 | 0.062 ¦ 0.071 | 0.137 ¦ 0.186 | 0.137 ¦ 0.186
605_5 (4.5 m) | 0.099 ¦ 0.241 | 0.115 ¦ 0.241 | 0.177 ¦ 0.439 | 0.184 ¦ 0.439
Limits
1. Validation runs come from the 17 training storms, so there the new input can simply recognise the storm. The unseen storms are the test: all 20 storm-by-cell comparisons improve.
2. Dynamic labels: GeoClaw is still 13–17 % low, and the 6-hour count on the two largest storms is 10–20 % low.
3. With the storm-size input, per-site timing inputs no longer help on these 17 storms: mean log loss on the unseen storms is 0.125 without them and 0.139 with (dynamic labels); 0.057 and 0.060 (static).
Mean of seeds 1 and 2; non-seed sites. Seeds differ by more than 0.02 in count error only for 605_5, static + timing (0.07 and 0.11). scripts/week29_context_table_v1.py.
Say: Only if asked. Every unseen storm improves in every cell. What is left: the GeoClaw map and the first six hours of the largest storms under dynamic labels, and one open question, which is whether the per-site timing inputs still earn their place once the model knows the storm's size.
Notes: Only if asked. Every unseen storm improves in every cell. What is left: the GeoClaw map and the first six hours of the largest storms under dynamic labels, and one open question, which is whether the per-site timing inputs still earn their place once the model knows the storm's size.

## Slide 10
Backup: old 17 against 57 storms, log loss on each unseen GISSR storm
Chart: Static labels, mask input
| 2.10 | 2.17 | 2.44 | 2.78 | 3.12 | 3.37 | 3.46 | 3.75* | 3.80* | 4.13* | 4.46* | 4.72*
17 storms | 0.0603 | 0.061 | 0.0891 | 0.0929 | 0.0942 | 0.096 | 0.0981 | 0.1133 | 0.1176 | 0.1315 | 0.1544 | 0.1978
57 storms | 0.0918 | 0.0926 | 0.0913 | 0.0816 | 0.0793 | 0.0793 | 0.0798 | 0.0816 | 0.0814 | 0.0816 | 0.0936 | 0.1272
lookup from 57 storms | 0.0206 | 0.0194 | 0.0842 | 0.1099 | 0.0788 | 0.0716 | 0.0698 | 0.0713 | 0.0668 | 0.0634 | 0.0777 | 0.0789
17 + storm size | 0.0127 | 0.012 | 0.081 | 0.0581 | 0.0567 | 0.0548 | 0.056 | 0.0626 | 0.0653 | 0.0767 | 0.1003 | 0.1293
57 + storm size | 0.0177 | 0.0198 | 0.0773 | 0.0576 | 0.0557 | 0.0533 | 0.0542 | 0.0563 | 0.055 | 0.0551 | 0.0659 | 0.088
Chart: Dynamic labels, timing inputs
| 2.10 | 2.17 | 2.44 | 2.78 | 3.12 | 3.37 | 3.46 | 3.75* | 3.80* | 4.13* | 4.46* | 4.72*
17 storms | 0.1026 | 0.0837 | 0.1342 | 0.1562 | 0.1744 | 0.2438 | 0.2614 | 0.2994 | 0.2241 | 0.259 | 0.4256 | 0.3178
57 storms | 0.141 | 0.1323 | 0.1509 | 0.1582 | 0.1586 | 0.1861 | 0.1775 | 0.214 | 0.1659 | 0.1583 | 0.2583 | 0.1794
lookup from 57 storms | 0.0614 | 0.024 | 0.1057 | 0.2034 | 0.1267 | 0.1565 | 0.1317 | 0.2238 | 0.1485 | 0.1272 | 0.2916 | 0.0756
17 + storm size | 0.0544 | 0.0147 | 0.0983 | 0.0964 | 0.1256 | 0.1703 | 0.1868 | 0.1417 | 0.1125 | 0.1175 | 0.1841 | 0.1455
57 + storm size | 0.0443 | 0.0237 | 0.0964 | 0.1037 | 0.1143 | 0.136 | 0.1251 | 0.1022 | 0.1047 | 0.0809 | 0.1327 | 0.0849
Read it as: the gap between 17 and 57 storms opens on the right, above the old range. The 57 + storm size line sits below the lookup on 10 (static) and 11 (dynamic) of the 12 storms; the lookup wins at 4.72 m.
One seed per line. GeoClaw 2050 (not shown): static 0.096 / 0.087 / 0.058 / 0.061, dynamic 0.298 / 0.245 / 0.194 / 0.143 in the order 17, 57, 17 + size, 57 + size; lookup 0.154 and 0.444.
Say: Only if asked. On the left of each chart, storms the old set already covered: more storms change little or hurt. On the right, storms bigger than the old set had: more storms help a lot.
Notes: Only if asked. On the left of each chart, storms the old set already covered: more storms change little or hurt. On the right, storms bigger than the old set had: more storms help a lot.

## Slide 11
Backup: predicted ÷ simulated failures by 96 h on each unseen storm
unseen storm (1.00 = correct) | static: 17 storms | static: 57 storms | static: 17 + storm size | static: 57 + storm size | dynamic: 17 storms | dynamic: 57 storms | dynamic: 17 + storm size | dynamic: 57 + storm size
new storm (2.10 m) | 3.74 | 4.86 | 1.05 | 1.40 | 3.45 | 4.51 | 0.76 | 1.26
914_6 (2.17 m) | 3.29 | 4.23 | 1.08 | 1.52 | 3.88 | 5.17 | 1.03 | 1.57
new storm (2.44 m) | 0.91 | 1.10 | 1.06 | 1.09 | 1.02 | 1.34 | 0.89 | 1.10
new storm (2.78 m) | 0.77 | 0.89 | 1.03 | 1.01 | 0.95 | 1.13 | 0.98 | 1.05
new storm (3.12 m) | 0.77 | 0.87 | 1.02 | 1.00 | 0.86 | 1.05 | 0.96 | 1.12
258_9 (3.37 m) | 0.78 | 0.87 | 1.03 | 1.01 | 0.70 | 0.82 | 0.90 | 1.00
new storm (3.46 m) | 0.78 | 0.88 | 1.03 | 1.01 | 0.65 | 0.77 | 0.85 | 0.92
808_27 (3.75 m) | 0.78 | 0.87 | 1.01 | 1.01 | 0.71 | 0.77 | 0.95 | 0.97
new storm (3.80 m) | 0.78 | 0.87 | 1.00 | 1.00 | 0.73 | 0.80 | 1.01 | 1.02
new storm (4.13 m) | 0.80 | 0.88 | 1.00 | 1.00 | 0.71 | 0.80 | 1.00 | 0.99
605_5 (4.46 m) | 0.82 | 0.89 | 1.02 | 1.00 | 0.72 | 0.79 | 1.01 | 0.99
new storm (4.72 m) | 0.80 | 0.86 | 1.00 | 0.96 | 0.71 | 0.79 | 1.03 | 0.98
GeoClaw 2050 (3.48 m) | 0.79 | 0.86 | 1.02 | 0.99 | 0.62 | 0.69 | 0.82 | 0.86
Red: more than 20 % off. With the storm-size input, the 17-storm model misses on one storm (dynamic labels, 2.10 m) and the 57-storm model on the two smallest storms under both label types.
Non-seed sites, mean over each storm's 1,000 runs, one seed per column. The 2.44 m storm sits where the cascade either takes off or does not: per-run count error there is about 0.5 for every model and for the lookup.
Say: Only if asked. The storm-size input brings almost every storm to within a few percent. The open point is the smallest storms when we train on all 57.
Notes: Only if asked. The storm-size input brings almost every storm to within a few percent. The open point is the smallest storms when we train on all 57.