## Slide 1
1 · WHERE WE STARTED
Last week you liked the dynamic cascade model, and asked for two things
1
Numbers
How good is the fast model, in numbers a reader can use?
2
More storms
Make more flood maps with Gwyn's model, run the simulator on them, train on old + new, and compare.
Fast model = the neural network that imitates the simulator. It answers in 11 milliseconds; one simulator run takes 0.2 to 1.5 seconds.
Say: This week follows your two requests, in that order.
Notes: Last week you liked the dynamic cascade model and asked for two things. First, numbers: how good is the fast model. Second, more flood maps from Gwyn's GISSR model, the simulator run on them, then train on old plus new and compare. I will go through them in that order. The first request turned up a problem, and most of the week went into understanding and fixing it.

## Slide 2
2 · ASK 1: THE NUMBERS
The fast model knows which sites fail and when, but not how many
Which sites fail
Good
Ranking score 0.92–0.93
(1.0 is perfect)
When they fail
Good
Right time window for
73–86 % of failing sites
How many fail
Poor
Count is off by 41–54 %.
A simple lookup table: 19 %
No retraining: the 8 models we already had, scored against the simulator and against simple baselines.
Say: Two things work. One does not: the size of the cascade.
Notes: I built a scoring tool and ran it on the eight models we already had, with no retraining. The model is good at which sites fail: ranking score 0.92 to 0.93. It is good at when: for 73 to 86 percent of failing sites it picks the right time window. But it is poor at how many sites fail: the count is off by 41 to 54 percent. A simple lookup table, which just reuses the most similar training storm, is off by only 19 percent. I had predicted the model would beat that table. It did not, and that miss is what led to the rest of the week.

## Slide 3
3 · WHAT THE NUMBERS TOLD US
It reads a small storm as a big one, and big storms as smaller
Chart: Predicted ÷ simulated failures on five unseen storms (1.0 = correct)
| Small storm (2.2 m) | 3.4 m | GeoClaw map | 3.7 m | Largest (4.5 m)
Predicted ÷ simulated failures | 3.8 | 0.7 | 0.62 | 0.7 | 0.72
Small storm: almost 4 times the real number of failures.
Big storms: about a third too few.
So: the model gives something like an average answer, whatever the size of the storm.
Say: Too many for the small storm, too few for the big ones: it is answering with an average.
Notes: This is the problem in one picture. Each bar is one storm the model never saw. A bar at 1.0 would be correct. For the small storm the model predicts almost four times too many failures. For the big storms it predicts about a third too few. So it behaves as if it gives roughly the same, average answer whatever the size of the storm. The question was why.

## Slide 4
4 · WHY IT HAPPENS
Each site only sees two links away, so most sites never see the flood
Flooded site
1 or 2 links away:
these sites can see the flood
Further away: they see nothing,
in a small storm or a big one
Sites too far to see any flooded site
59–88 %
of all 6,231 sites, in every storm
Same input → same answer. These sites get one average answer in every storm.
Shown on the model itself: 3,481 sites got identical outputs in a small and a large storm. 24 of them fail in the small storm, 610 in the large one.
Say: A cell tower in the Bronx is told nothing about whether Lower Manhattan is under water.
Notes: Here is the reason. The model passes information along the network for two links only. A site within two links of a flooded site can see the flood. A site further away sees nothing. And most sites are further away: 59 to 88 percent of them, depending on the storm. Think of a cell tower in the Bronx with nothing flooded nearby. It is told nothing about whether Lower Manhattan is under water. So it gets exactly the same input in a small storm and in a big one, and the model must give it the same answer: an average. I checked this on the model itself: 3,481 sites got identical outputs in a small storm and a large one, although 24 of them fail in the small storm and 610 in the large one.

## Slide 5
5 · THE NEW STRATEGY
The fix: tell every site how big the storm is
Before
Each site knows only what is within two links of it.
→
Now
Every site also gets 7 numbers about the whole storm: how much of each of the six systems is flooded, and the total.
Not giving it the answer: the 7 numbers come only from the flood map. Nothing from the cascade outcome.
Tested fairly: 5 predictions written down before training. Same 17 storms, same model, one switch on or off.
Say: Like telling every operator, before Sandy, how much of each system will be under water.
Notes: If the problem is that far-away sites do not know the size of the storm, the simplest fix is to tell them. Every site now also receives seven numbers that describe the whole storm: how much of each of the six infrastructure systems the water knocks out, and the total. Sandy version: every operator in the city is told beforehand how much of each system will be under water. Two things matter here. First, this is not giving the model the answer: the numbers come only from the flood map, which the model already had as an input. Second, I wrote down five predictions before training, so the test could fail. Everything else stayed the same: same 17 storms, same model.

## Slide 6
6 · WHAT THE NEW NUMBERS SAY
It worked: predicted failures are now close to the simulator
Chart: Predicted ÷ simulated failures on five unseen storms (1.0 = correct)
| Small storm (2.2 m) | 3.4 m | GeoClaw map | 3.7 m | Largest (4.5 m)
Before | 3.8 | 0.7 | 0.62 | 0.7 | 0.72
With the storm-size input | 1.05 | 0.91 | 0.83 | 0.96 | 1.02
Count error
41–54 % → 15–17 %
Small storm
3–4 times → 1.1 times
Wins against the lookup table
7 of 24 → 23 of 24
Say: All five written predictions passed, and the model now beats the lookup table.
Notes: It worked, and it worked the way I had written down beforehand: all five predictions passed. Look at the small storm: from almost four times too many failures to about 1.1 times. The big storms moved from about a third too few to within a few percent. Count error on validation fell from 41 to 54 percent down to 15 to 17 percent. And the model now beats the lookup table in 23 of 24 comparisons; before it won 7. One honest limit: under dynamic labels the GeoClaw map is still about 17 percent low, which you can see in the middle bar. The detailed deck has every storm and the limits.

## Slide 7
7 · ASK 2: MORE STORMS
48 new storms from Gwyn's model, chosen by a rule written in advance
Chart: Storm speed (hours a site is wet before the peak) against storm size
| 1.911 | 1.922 | 1.922 | 2.017 | 2.102 | 2.15 | 2.166 | 2.272 | 2.292 | 2.369 | 2.563 | 2.632 | 2.797 | 3.092 | 3.24 | 3.372 | 3.444 | 3.64 | 3.745 | 4.458 | 1.935 | 2.002 | 2.07 | 2.138 | 2.205 | 2.272 | 2.339 | 2.408 | 2.477 | 2.544 | 2.614 | 2.684 | 2.755 | 2.807 | 2.88 | 2.959 | 3.011 | 3.089 | 3.142 | 3.232 | 3.299 | 3.342 | 3.407 | 3.498 | 3.557 | 3.632 | 3.687 | 3.759 | 3.827 | 3.89 | 3.963 | 4.027 | 4.105 | 4.153 | 4.23 | 4.297 | 4.363 | 4.437 | 4.508 | 4.572 | 2.103 | 2.439 | 2.777 | 3.116 | 3.458 | 3.8 | 4.13 | 4.722
20 old storms | 1.86 | 1.8 | 1.89 | 1.6 | 2.22 | 2.46 | 1.69 | 2.08 | 2.42 | 2.6 | 1.52 | 2.2 | 12.92 | 3.54 | 3.28 | 2.55 | 13.95 | 14.48 | 13.45 | 26.38
40 new, for training | 2 | 12.05 | 2 | 11.91 | 2 | 11.96 | 2 | 11.9 | 1.99 | 11.99 | 2 | 12.02 | 2 | 12 | 2.01 | 11.91 | 2.05 | 12.02 | 1.99 | 11.96 | 2 | 11.77 | 2.01 | 11.41 | 2.02 | 12.01 | 1.99 | 12.08 | 2.05 | 12.6 | 2.42 | 11.97 | 2.42 | 11.91 | 2.98 | 12.29 | 2.62 | 11.87 | 2.63 | 12.72
8 new, kept unseen | 3.77 | 10.65 | 3.96 | 9.26 | 4.02 | 6.68 | 4.06 | 6.72
48 = 40 + 8. 40 to train on, 8 the model never sees.
1,000 simulator runs on every storm. All finished, all checks passed.
Bigger storms: up to 4.6 m. The old training storms stopped at 3.6 m.
Size and speed separated: in the old storms the big ones were always the slow ones.
Say: Grey dots: big storms were always slow. Purple dots: fast and slow at every size.
Notes: For your second request I chose 48 new storms from Gwyn's catalogue of about 74,000, by a rule written before I saw any cascade result: evenly spaced sizes, alternating fast and slow. Forty are for training and eight are held out. I ran the simulator 1,000 times on each one, and everything passed its checks. The chart shows what they add. In the old storms, the grey dots, the big storms were always the slow ones, so the model could not tell size from speed. The new storms, in purple, have fast and slow storms at every size, and they go up to 4.6 metres where the old training set stopped at 3.6. One caution: these maps come from the same flood model, so they add new sizes and timing, not new places where the water goes.

## Slide 8
8 · OLD STORMS AGAINST OLD + NEW
Each step lowers the error. Together they cut it by half
Chart: Prediction error on 13 unseen storms (lower is better)
| 17 storms (old) | 57 storms (old + new) | Lookup table | 17 storms + storm size | 57 storms + storm size
Error on 13 unseen storms | 0.229 | 0.179 | 0.163 | 0.126 | 0.099
More storms help, most for storms bigger than any in the old set (26–44 % lower there).
But not enough alone: the lookup table (red) is still better.
With the storm-size input the model gets under the lookup. With both, error is about half.
Interim. One training run each. The run using all new simulator runs was cancelled by the cluster.
Say: Read the bars left to right as a staircase. The red bar is the one to beat.
Notes: This is the comparison you asked for: the same model trained on the old storms and on old plus new, tested on 13 storms it never saw. Read the bars left to right as a staircase. Old storms only: 0.23. Adding the new storms: 0.18, and the gain is largest for storms bigger than any in the old set, 26 to 44 percent lower there. But more storms alone do not get under the lookup table, the red bar, because they do not fix the size problem. The storm-size input does: 0.13. And with both, 0.10, less than half of where we started. This is the dynamic model; the static one shows the same order. I call it interim: each bar is one training run, and the run that uses all of the new simulator runs was cancelled by the cluster part-way, so I report only what finished.

## Slide 9
9 · WHERE WE ARE NOW
The model now gets which, when and how many. Three things are still open
What we know now
The model was missing one fact: the size of the storm. Giving it fixes the count.
It now beats the lookup table in 23 of 24 comparisons.
More storms help most for storms bigger than any it had seen.
Still open
Old + new is interim: one run each, and one training set was cancelled by the cluster.
Smallest storms: with 57 storms and the fix, the two smallest are over-counted by 26–57 %.
Dynamic labels: the GeoClaw map is still 13–17 % low.
Say: The main result is solid: two runs each, predictions written first. The old-against-new part is interim.
Notes: To sum up. The model was missing one fact, the size of the storm, and giving it that fact fixes the count. That result is solid: two training runs per setting, predictions written first, all passed, and the model now beats the lookup table in 23 of 24 comparisons. More storms help most for storms bigger than anything in the old set. Three things are still open, and I would rather say them myself. The old-against-new comparison is interim: one run each, and one training set was cancelled. With 57 storms plus the fix, the two smallest unseen storms are over-counted by 26 to 57 percent, and I do not know why yet. And under dynamic labels the GeoClaw map is still 13 to 17 percent low.

## Slide 10
10 · NEXT
Next steps, and four decisions I need from you
Next steps
1. Finish the old + new comparison: the cancelled runs and a second run of each.
2. Make the storm summary follow the clock, hour by hour.
3. Test on flood maps with new patterns, not only bigger ones.
Decisions
Surge clock: keep it at the flood's peak, or start at first arrival of water?
Week 23 numbers: quote them "on a 6-hour grid", or rerun on a 3-hour grid?
Reporting rule: tipping share always quoted with its grid.
New: Gwyn's depth tables are in the public repo. Is that acceptable?
Say: Three next steps. Then stop and wait for the four answers.
Notes: Three next steps. First, finish the old plus new comparison: the runs the cluster cancelled, and a second run of each so I can say how much the results move. Second, make the storm summary follow the clock, because today it is one set of numbers for the whole storm and the first six hours of the largest storms are still a little low. Third, test on flood maps that look different, not just bigger, because GISSR storms differ only in size and timing. And I need four decisions. Three are open from September: where the phone-demand surge clock starts, how to quote the Week 23 numbers, and the reporting rule for the tipping share. One is new: the new depth tables come from Gwyn's unpublished model and are in the public repository, as the first twenty are. Is that acceptable? One more question for Gwyn herself: her 20 maps are reproduced by one-hour time steps; I would like to confirm that is what she intended.